Release date: March 2014

## INSTRUCTION MANUAL

# FOCUS ”D”

### SMT Convection Rework System

|  | P/N X-DOC215 14-03-14 Rev. A |
| --- | --- |

| 650 Scranton Pocono Hwy., Covington Twp., PA 18444, USA Tel: (570) 842-2812 Fax: (570) 842-4290 www.bokar.com, www.smt-tool.com www.ESDmeters.com, www.ESDlabcoats.com E-Mail: bokar@bokar.com |  |
| --- | --- |

### FOCUS ”D” SMT Convection Rework System

#### TABLE OF CONTENTS

PAGE

I.	PACKAGING 	3

II.	UNPACKING	3

III.	SET-UP AND INSTALLATION	3

IV.	SYSTEM DESCRIPTION and APPLICATION	5

V.	STANDARD NOZZLES	8

VI.	TECHNICAL SPECIFICATIONS 	11

VII.	SPARE PARTS LIST	12

VIII.	OPTIONAL ACCESSORIES	12

FIG. 1 VIEW OF THE CONTROL PANEL

FIG. 2 VIEW OF THE BACK PANEL

##### PACKAGING

The box contains as follows:

  - FOCUS ”D” Base Unit with XHT-12 Hot Air Tool

  - XTH-1 Tool Holder

  - Manual

  - Guarantee card

Note: You need to order the required nozzle to use the system after unpacking.

##### UNPACKING

Prior to use of the system, please check if the system is complete. Should you notice that any items are missing, please notify us, giving the details of model number, voltage, date of purchase, where purchased and what is missing.

#### Attention: When unpacking, please be careful and read the manual prior to turning the system “ON”. Please check if the voltage of the System corresponds with the voltage of your available supply. Connection to incorrect supply voltage may cause damage to the System!

##### SET-UP AND INSTALLATION

  - The system should be located on stable work surface.

  - Mount the Hand Piece holder XTH-1 on the right or left side of the FOCUS “D”  base unit.

  - Select the proper nozzle to match the component which you need to rework.

  - Install the nozzle onto the XHT-12 tool.

  - Place the XHT-12 Hand Piece into the holder.

  - Connect the foot switch to the connector on the back panel of the FOCUS “D”  base unit (optional).

  - Check if the Power Switch is in “0” (OFF) position.

  - Connect the AC power to a suitable AC power outlet.

  - Turn the Power Switch “ON”

  - Adjust the air flow (valve on the left/bottom of the front panel) to desired value.

You will see the air flow in l/min on the flow meter above the Air Control Valve

  - Adjust temperature to a desired value by pushing in and turning the front panel control knob. When you arrive to desired setting (shown on the display) push the knob inwards to confirm the setting.

CAUTION

To insure operator safety, the AC supply receptacle must be checked for proper grounding before connecting the Rework System this outlet.

###### USING FOCUS“D” REWORK SYSYTEM

- Turning FOCUS”D” “ON”:

  - Plug the system power cord into an appropriate AC supply receptacle.

  - Set the unit POWER Switch to “ON” position.

  - Press On/Off key to start the unit.

- Turning FOCUS”D” “OFF”:

  - Press ON/OFF key.

  - The display will turn off.

- VIEW SET TEMPERATURE

  - Press FOCUS”D” knob momentarily.

  - The display will show blinking  set temperature.

  - Press the knob one more time to exit SET temperature verification.

- SET TEMPERATURE CHANGE

  - Press FOCUS”D” knob momentarily.

  - The display will show blinking  set temperature.

  - Set the required value rotating the control knob counterclockwise to decrease or clockwise to increase desired SET Temperature.

  - Push-in the knob to finalize the entry.

Note: If you do not press the knob, the change will not be recorded by the system.

You may exit the Temperature Set process by pressing ESC (Escape) button.

- COOLING  MODE

  - Press COOL key.

  - The system heater will be turned off immediately; the display will show  for few seconds and then show   current temperature of the cooling air.           To speed-up the cooling the fan RPM increases for a duration of the cooling cycle.

  - To turn on the Cooling, press “ON/OFF” key.

##### SYSTEM DESCRIPTION and APPLICATION

FOCUS “D” Series is a low-cost convection rework system with closed loop temperature control, air flow gauge and component vacuum pick up subsystem.

Features:

- Closed-loop, variable temperature control

- Fully grounded and static-safe

- Optical isolation with zero voltage switching

- Thin, stainless steel, low mass nozzles secured by set screws.

- Ergonomically designed, ESD Safe Hand piece with the following advantages:

  - patented heater with air equalizer

  - heater ON-OFF Switch on the handpiece

  - vacuum tube positioning at operator fingertips

  - patented, angled hand tool top to reduce cable pull during hand held operations to increase accuracy of the hot air stream aim and to ease operator fatigue during system use

- Over 40 standard nozzles available for this system and custom nozzles available on with quick deliveries at nominal extra cost.

- Possibility to attach XFQ quick connect adapter to use with X type quick replacement nozzles.

- Standard units are self-contained (with integral air pump). Units for use with Nitrogen available as part number FOCUS”D”-N2.

#### PROGRAMMING OF THE UNIT

###### CHANGING OR VIEWING SYSTEM SETTINGS

- Press for 3 sec. Temperature Set Control Knob on the Front Panel of the unit. The displays will show  for few seconds and then will show the first system setting, LOCK function.

- To view and/or change the System Settings rotate the Control knob clockwise to the next parameter to be viewed or set.

Note: Rotating the control knob counter clockwise will show the set parameters in the reverse order.

|  | Lock Feature The lock feature is used to limit the accessibility of an operator to Machine settings. Changes may only be made when a 4-digit code is entered. -- When set to OFF no code is needed to make changes. -- When set to On a code is required to make changes. The unit is delivered from the Factory unlocked. (LOCK setting: ). ( Please see below in this manual for more detailed information on this function). |
| --- | --- |
|  | Code Change See below for more information. |
|  | Temperature Scale Setup -- temperature in Celsius (°C). -- temperature in Fahrenheit (°F). Factory setting: |
|  | Foot Switch -- System starts heating when the Foot Switch is pressed and stops heating when the Foot Switch is released. -- Heating controlled from the ON/OFF switch on the front panel or the switch on the hand piece. Foot Switch activation is disabled. Factory setting: |
|  | Sound ON/OFF -- When set to ON the beep will be heard when pressing the keys. -- When set to OFF the unit will not make any sound. Factory setting: |
|  | Not available to the user. |

###### Nozzle Offset Entry:  (Important to understand and use).

When the system is Powered ON the nozzle offset can be entered.

    - Press ESC key and “Temperature Control Knob” simultaneously.

    - The display will show:  for one second and will blink displaying “0” degree to prompt you to enter a desired offset value. Turn the Control knob clockwise to increase or counter clockwise to decrease the value.

Push-in the knob when the display shows the value which you have intended to pre-set.

Note1: The maximum offset value which can be pre-set is 50 deg. C.

Note2: Please remember that the temperature of the air at the end of your nozzle

depends on the nozzle configuration and will be different for different nozzles.

For best temperature accuracy during your work pre-set proper offset value for

each nozzle type.

###### Protection against unauthorized change of pre-programmed parameters

When system is unlocked system feature  is set to . All parameters and system features can be altered without restrictions. When system feature  is set to , the system will ask for a code number when someone will try to change pre-programmed values.

The Display will show:  (First digit blinking). To unlock the system, previously selected code number must be entered. If incorrect value of the code number is entered, the display will show  and sound will be heard for about one second. The system will re-set to the state it was in before an attempt to change the parameter. Properly entered code will unlock the system and allow for parameters change until the system is locked again or until the system is turned-off by POWER switch (or by unplugging the unit from the wall outlet). It is sufficient to enter an appropriate code once during the time when the system is powered.

Special CODE numbers used by the system:

1234- factory set code on delivery of the system to a customer.

XXXX- „emergency code”; (call or e-mail Bokar International to obtain it. Proof of purchase will be required to release the emergency code). This emergency code will allow changing the code when entered in place of the old code.

YYYY- „master code”; this is manufacturers code which can be used in parallel or instead off the user code. Use of the “master code” does not interfere with currently used code numbers.

It is available only for authorized Bokar Factory personnel.

# FIRMWARE UPGRADE

#### Checking firmware revision and SN in the device.

- Connect the power cord

- Turn the Power Switch to the "ON" position.

- Press and hold “Esc” button.

- After a few second the displays will show: Info and two sets of numbers.

The first set = Software Revision and the second number = the unit’s serial number.

| Info | Description |
| --- | --- |
| 1.08 | Software revision |
| 545 | Serial number |

#### Unit Re-programming procedure

Turn the Power Switch to the "OFF" position.

Connect X485USB converter to the DATASTORE connector and to PC.

Press and hold “Temperature Control Knob” on the Front Panel.

Turn the Power Switch to the "ON" position.

Release the “Temperature Control Knob”.

Displays will show: “----“.

Run the newest program flasher.exe (on your PC).

Select proper port number and press “Connect”.

If connection is established, you will see: “Vendor name: Bokar international”

If not please reconnect the USB cable to another USB port on your PC.

When you establish the connection between the unit and your PC your PC screen will show

as below:

Select “File” from the menu and choose the file with extension (*.hex).
For example: “FOCUS_D_X10HD05D_code.hex”

Press “Open”

Follow the instructions on your PC screen.

Press “Write”

If re-programming was successful, the message “Write successful” and                                  “Would you like to run application” will appear on the screen

Press “Yes” to confirm.

##### STANDARD NOZZLES (Custom nozzles available upon request)

##### Attention: When ordering nozzles for use without the XQF quick connect please add “L” at the end of the Part Number. E.g.: XNB-7x7 L

|  | BGA/CSP FOCUS SERIES CONVECTION NOZZLES |
| --- | --- |

| P/N | Nozzle Number | A (inside diameter) | Suggested Package |
| --- | --- | --- | --- |
|  |  | Inch | mm |  |
| X1NB 7X7 | 100A | 0.315 | 8 | BGA16, BGA25 |
| X1NB 8X8 | 100 | 0.393 | 10 | BGA16, BGA25 |
| X1NB 10,5X10,5 | 100B | 0.413 | 10,5 | BGA16, BGA25 |
| X1NB 7,5X9 | 100C | 0.295x0.354 | 7,5x9 | BGA16, BGA25 |
| X1NB 12,4X12,4 | 101A | 0.488 | 12,4 | BGA49, BGA 64 |
| X1NB 12X12 | 101 | 0.551 | 14 | BGA49, BGA 64 |
| X1NB 13,6X13,6 | 102A | 0.512 | 13 | BGA49, BGA 64 |
| X1NB 13X13 | 102 | 0.590 | 15 | BGA49, BGA 64 |
| X1NB 15X15 | 103 | 0.669 | 17 | BGA81, BGA100 |
| X1NB 17X17 | 104 | 0.748 | 19 | BGA121 |
| X1NB 19X19 | 105 | 0.787 | 21 | BGA141, BGA121 |
| X1NB 23X23 | 106 | 0.984 | 25 | BGA169 |
| X1NB 27X27 | 107 | 1.142 | 29 | BGA324, BGA225, BGA289 |
| X1NB 35X35 | 108 | 1.457 | 37 | BGA529, BGA484 |
| X1NB 38X38 | 109 | 1.575 | 40 | BGA576, BGA625 |
| X1NB 40X40 | 110 | 1.654 | 42 | BGA625, BGA676 |

|  | QFP/BQFP FOCUS SERIES CONVECTION NOZZLES |
| --- | --- |

| P/N | Nozzle Number | A | B | C | D | Suggested Package |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | inch | mm | inch | mm | inch | mm | inch | mm |  |
| X1NQ 12x12 | 200 | .472 | 12 | .551 | 14 | .472 | 12 | .551 | 14 | QFP64, QFP48, QFP80, BQFP28 |
| X1NQ 14x14 | 201 | .591 | 15 | .677 | 17,2 | .591 | 15 | .677 | 17,2 | SQFP100, TQF100 |
| X1NQ 14x20 | 202 | .591 | 15 | .665 | 16,9 | .827 | 21 | .906 | 23 | QFP128, QFP80, QFP100 |
| X1NQ 16x16 | 203 | .629 | 16 | .826 | 21 | .629 | 16 | .826 | 21 | BQFP100T25, QFPT63 |
| X1NQ 17.5x17.5 | 204 | .590 | 15 | .728 | 18,5 | .590 | 15 | .728 | 18,5 | BQFP84 |
| X1NQ 24x24 | 205 | .827 | 21 | .953 | 24,2 | 0.827 | 21 | .953 | 24,2 | BQFP132, FQFP176 |
| X1NQ 28x28 | 206 | 1.142 | 29 | 1.220 | 31 | 1.142 | 29 | 1.220 | 31 | QFP128, SQFP208 |
| X1NQ 32x32 | 207 | 1.220 | 31 | 1.315 | 33,4 | 1.220 | 31 | 1.315 | 33,4 | QFP184T, FQFP408 |
| X1NQ 37x37 | 208 | 1.220 | 31 | 1.457 | 37 | 1.220 | 31 | 1.457 | 37 | BQFP196 |
| X1NQ 40x40 | 209 | 1.535 | 39 | 1.654 | 42 | 1.535 | 39 | 1.654 | 42 | BQFP244 |

|  | PLCC FOCUS SERIES CONVECTION NOZZLES |
| --- | --- |

| P/N | Nozzle Number | A | B | C | D | Suggested Package |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | inch | mm | inch | mm | inch | mm | inch | mm |  |
| X1NP 7,3x12,5 | 300 | .272 | 6,9 | .354 | 9 | .272 | 6,9 | .551 | 14 | PLCC 7,3X12,5 |
| X1NP 11,5x11,5 | 301 | .394 | 10 | .512 | 13 | .394 | 10 | .512 | 13 | PLCC28 |
| X1NP 11,5x14 | 302 | .591 | 15 | .591 | 15 | .394 | 10 | .512 | 13 | PLCC 11,5X14 |
| X1NP 17,5x17,5 | 303 | .591 | 15 | .728 | 18,5 | .591 | 15 | .728 | 18,5 | PLCC44 |
| X1NP 20x20 | 304 | .748 | 19 | .827 | 21 | .748 | 19 | .827 | 21 | PLCC52 |
| X1NP 25x25 | 305 | .945 | 24 | 1.024 | 26 | .945 | 24 | 1.024 | 26 | PLCC68 |
| X1NP 30X30 | 306 | 1.142 | 29 | 1.220 | 31 | 1.142 | 29 | 1.220 | 31 | PLCC84 |
| X1NP 11,5x25 | 307 | .945 | 24 | 1.354 | 34,4 | .394 | 10 | .480 | 12,2 | PLCC 11.5x25 |

|  | SO/SOL FOCUS SERIES CONVECTION NOZZLES |
| --- | --- |

| P/N | Nozzle Number | A | D | Suggested Package |
| --- | --- | --- | --- | --- |
|  |  | inch | mm | inch | mm |  |
| X1NS 4.4x10 | 400 | .394 | 10 | .189 | 4,8 | SO16 |
| X1NS 5.6x13 | 402 | .591 | 15 | .224 | 5,7 | SSOP8T |
| X1NS 7.6x15 | 403 | .630 | 16 | .283 | 8,2 | SOL20/26, TSOP20/24 |
| X1NS 7.6x18 | 404 | .748 | 19 | .283 | 8,2 | TSOP24 |
| X1NS 7.6x12.7 | 405 | .472 | 12 | .323 | 8,2 | SOL20, TSOP28 |
| X1NS 19x8 | 406 | .315 | 8 | .748 | 19 | TSOP32 |
| X1NS 8.6x18 | 407 | .748 | 19 | .343 | 8,7 | TSOP28/32 |
| X1NS 18.5x12 | 408 | .748 | 15 | .728 | 19,5 | TSOP40/48 |
| X1NS 13x28 | 409 | 1.142 | 29 | .531 | 13,5 | PSOP44 |
| X1NS 21X11.3 | 410 | .827 | 21 | .445 | 11,3 | SOP32 |

|  | SOJ FOCUS SERIES CONVECTION NOZZLES |
| --- | --- |

| P/N | Nozzle Number | A | D | Suggested Package |
| --- | --- | --- | --- | --- |
|  |  | inch | mm | inch | mm |  |
| X1NS 15x8.2 | 401 | .591 | 15 | .323 | 8,2 | SOJ20 |

#### DISCRETE NOZZLES

Five sizes to choose from. X1ND-3 and X1ND-4 for use when high air/gas flow is needed.

| X1ND-4 | X1ND-5 |
| --- | --- |

##### TECHNICAL SPECIFICATIONS

| Input Voltages | Models 115V AC and 230V AC |
| --- | --- |
| Power Consumption | 500W |
| Fuse | 5A Slow-Blow 5mm x 20mm |
| Heater | Resistive, 450W line voltage |
| Heater Control | Closed-Loop Thermocouple sensor feedback |
| Air Source | High efficiency diaphragm pump |
| Air Flow | Variable, 3 – 20 l/min, air flow controlled by the valve located on the front panel |
| Temperature | 150 ºC – 450 ºC (302 ºF – 842 ºF) |
| Weight | 6kg (13.3 lbs) |
| System dimensions | 150mm x 220mm x 170mm (5.9” x 8.7” x 6.7”) |
| Packaged weight | 7.5kg (16.6 lbs) |

##### SPARE PARTS LIST

##### (Please consult the Distributor in your country)

##### FOCUS SERIES ACCESSORIES and recommended ADDITIONAL PRODUCTS to make rework easier and safer.

  - Range of Nozzles (see above)

| XFS-3 Foot Switch |  |
| --- | --- |
| XVCS Series (Vacuum Pick-Up Pad Set) are made of high temperature ESD silicone and have molded inside stopper to prevent vacuum tube from protruding though the cup. XVCW-10 Diameter: 10 mm (~.4 inch) XVCW-8 Diameter: 8 mm (~.315 inch) XVCW-6 Diameter: 6 mm (~.25 inch) XVCS-5 Set includes: XVCW-10 1 pcs, XVCW-8 2 pcs, XVCW-6 2 pcs XVCS-10 Set includes: XVCW-10 2 pcs, XVCW-8 4 pcs, XVCW-6 4 pcs | XVCW-10 XVCW-8 XVCW-6 |
| X-T1 Vacuum Pad Insertion/Removal Tool ( for the units with incorporated vacuum pick-up. |  |
| XNR-1 Nozzle Insertion Removal Tool |  |
| XNR-2 Hot Nozzle Handling Cup. Handy, simple tool to handle the nozzles when they are hot. |  |
| XNH-1 Nozzle holder |  |
| XNH-2 Nozzle holder (For large nozzles) |  |
| XU-1S or XU-1 Retractable Board Holder (Maximum board size 12” (305mm) x open end. |  |
| XK-1, XK-2 or XK-3 - Adjustable Tool Holder for precision movement of the tool up and down. XK-3 tool holder includes the rotation stage allowing for theta adjustment (rotation) of the tool. |  |
| X-600, X-1001 Convection Pre-heaters and X-600IR or X-1200IR Infrared preheaters made in USA. |  |
| XU-Mini Irregular Shape PCB Holder (e.g. Cellular Phone) |  |
| XU-5 Open Frame Board Holder with X-Y micrometer positioning for PCB fine adjustment. |  |

Other Recommended Products:

SMT: www.Assembly-SMT.com www.SMT-tool.com www.X-Reflow306.com, www.X-1003.com www.SMTrepair.com www.SMTFocus.com www.FineRework.com www.SMTdispenser.com www.BestBatchOven.com

ESD: www.ESDapparel.com www.ESDmeters.com www.ESDpackaging.net www.ZeroCharge.net www.No-Stat.com www.ESDchair.com www.ESDlabcoats.com www.ESDcarts.net www.ESDchair.com www.ESDbrushes.com

Other: www.SuperiorScrewdrivers.com www.Super-Iron.com Latest Additions: www.PCBprototypingRobot.com www.ECOguardCC.com

|  | BOKAR International 650 Scranton Pocono Hwy, PA 8444, USA |
| --- | --- |
| Tel: (570) 842-2812 Fax: (570) 842-4290 E-mail: bokar@bokar.com www.bokar.com |

# Text boxes

Temperature Set Control Knob

(Push and turn)

Heater Indicator

Hot Air Tool Connection

Flow Meter

Power Switch

Control switches

Air Flow Control

Factory Calibration Port

Fuse Holder

Foot Switch Connector

Power Cord

X1ND-1

X1ND-2

X1ND-3